Digital Integrated Circuits A Design Perspective
Digital Integrated Circuits
A Design Perspective
Jan M. Rabaey
Anantha Chandrakasan
Borivoje Nikolic
Designing Sequential
Logic Circuits
November 2002

---
Sequential Logic
Sequential Logic
2 storage mechanisms
• positive feedback
• charge-based

---
Naming Conventions
Naming Conventions
In our text:
  - a latch is level sensitive
  - a register is edge-triggered
There are many different naming conventions
  - For instance, many books call edge-triggered elements flip-flops
  - This leads to confusion however

---
Latch versus Register
Latch versus Register
Latch
stores data when
clock is low
Register
stores data when
clock rises
D
Q
D
Q
Clk
Clk
Clk
Clk
D
D
Q
Q

---
Latches
Latches

---
Latch-Based Design
Latch-Based Design
N latch is transparent
when  = 0
P latch is transparent
when  = 1

N
P
Logic
Latch
Latch
Logic

---
Timing Definitions
Timing Definitions
CLK
Register
t
D
Q
t
t
su
hold
D
DATA
CLK
STABLE
t
t
c
q
2
Q
DATA
STABLE
t

---
Characterizing Timing
Characterizing Timing
Latch
Register

---
Maximum Clock Frequency
Maximum Clock Frequency
Also:
tcdreg + tcdlogic > thold
tcd: contamination delay = minimum delay
tclk-Q + tp,comb + tsetup = T

---
Positive Feedback: Bi-Stability
Positive Feedback: Bi-Stability
1
1
o
o
V
V
5
2
i
V
1
o
V
5
2
i
V
V
i
1
A
C
B
V
o
2
V
i
1
=
V
o
2
V
o1
Vi2
V
i
2
=
V
o
1

---
Meta-Stability
Meta-Stability
Gain should be larger than 1 in the transition region

---
Writing into a Static Latch
Writing into a Static Latch
Use the clock as a decoupling signal,
that distinguishes between the transparent and opaque states
Forcing the state
(can implement as NMOS-only)
Converting into a MUX
D
CLK
CLK
D

---
Mux-Based Latches
Mux-Based Latches
Negative latch
(transparent when CLK= 0)
Positive latch
(transparent when CLK= 1)
CLK
size 12{Q= {overline { ital "Clk"}} cdot Q+ ital "Clk" cdot ital "In"} {}
size 12{Q= ital "Clk" cdot Q+ {overline { ital "Clk"}} cdot ital "In"} {}
1
0
D
Q
0
CLK
1
D
Q

---
Mux-Based Latch
Mux-Based Latch

---
Mux-Based Latch
NMOS only
Non-overlapping clocks

---
Master-Slave (Edge-Triggered) Register
Master-Slave (Edge-Triggered) Register
Two opposite latches trigger on edge
Also called master-slave latch pair

---
Master-Slave Register
Master-Slave Register
Multiplexer-based latch pair

---
Clk-Q Delay
Clk-Q Delay

---
Setup Time
Setup Time

---
Reduced Clock Load  Master-Slave Register
Reduced Clock Load
Master-Slave Register

---
Avoiding Clock Overlap
Avoiding Clock Overlap
X
CLK
CLK
Q
A
D
B
CLK
CLK
(a) Schematic diagram
CLK
CLK
(b) Overlapping clock pairs

---
Overpowering the Feedback Loop ─ Cross-Coupled Pairs
Overpowering the Feedback Loop ─
Cross-Coupled Pairs
NOR-based set-reset

---
Cross-Coupled NAND
Cross-Coupled NAND
Added clock
Cross-coupled NANDs
This is not used in datapaths any more,
but is a basic building memory cell

---
Sizing Issues
Sizing Issues
Output voltage dependence
on transistor width
Transient response

---
Storage Mechanisms
Storage Mechanisms
Dynamic (charge-based)
Static
CLK
D
Q
CLK

---
Making a Dynamic Latch Pseudo-Static
Making a Dynamic Latch Pseudo-Static

---
More Precise Setup Time
More Precise Setup Time

---
Setup/Hold Time Illustrations
Setup/Hold Time Illustrations
Circuit before clock arrival (Setup-1 case)

---
Setup/Hold Time Illustrations
Circuit before clock arrival (Setup-1 case)

---
Setup/Hold Time Illustrations
Circuit before clock arrival (Setup-1 case)

---
Setup/Hold Time Illustrations
Circuit before clock arrival (Setup-1 case)

---
Setup/Hold Time Illustrations
Circuit before clock arrival (Setup-1 case)

---
Setup/Hold Time Illustrations
Hold-1 case
0

---
Setup/Hold Time Illustrations
Hold-1 case
0

---
Setup/Hold Time Illustrations
Hold-1 case
0

---
Setup/Hold Time Illustrations
Hold-1 case
0

---
Setup/Hold Time Illustrations
Hold-1 case
0
size 12{ drarrow } {}

---
Other Latches/Registers: C2MOS
Other Latches/Registers: C2MOS
“Keepers” can be added to make circuit pseudo-static

---
Insensitive to Clock-Overlap
Insensitive to Clock-Overlap
V
V
V
V
DD
DD
DD
DD
M
M
M
M
2
6
2
6
M
M
0
0
4
8
X
X
D
Q
D
Q
M
M
1
1
3
7
M
M
M
M
1
5
1
5
(a) (0-0) overlap
(b) (1-1) overlap

---
Pipelining
Pipelining
Pipelined
Reference

---
Other Latches/Registers: TSPC
Other Latches/Registers: TSPC
Positive latch
(transparent when CLK= 1)
Negative latch
(transparent when CLK= 0)

---
Including Logic in TSPC
Including Logic in TSPC
Example: logic inside the latch
AND latch

---
TSPC Register
TSPC Register

---
Pulse-Triggered Latches An Alternative Approach
Pulse-Triggered Latches
An Alternative Approach
Ways to design an edge-triggered sequential cell:
Master-Slave Latches
Pulse-Triggered Latch
L1
L2
L
Data
Data
D
Q
D
Q
D
Q
Clk
Clk
Clk
Clk
Clk

---
Pulsed Latches
Pulsed Latches

---
Pulsed Latches
Hybrid Latch – Flip-flop (HLFF), AMD K-6 and K-7 :

---
Hybrid Latch-FF Timing
Hybrid Latch-FF Timing

---
Latch-Based Pipeline
Latch-Based Pipeline

---
Non-Bistable Sequential Circuits─ Schmitt Trigger
Non-Bistable Sequential Circuits─
Schmitt Trigger
VTC with hysteresis
Restores signal slopes

---
Noise Suppression using Schmitt Trigger
Noise Suppression using Schmitt Trigger

---
CMOS Schmitt Trigger
CMOS Schmitt Trigger
Moves switching threshold
of the first inverter

---
Schmitt Trigger Simulated VTC
Schmitt Trigger Simulated VTC
2.5
2.5
2.0
2.0
V
1.5
1.5
M
1
(V)
(V)
x
X
1.0
1.0
V
V
V
M
2
k
= 1
k
= 3
k
= 2
0.5
0.5
k
= 4
0.0
0.0
0.0
0.5
1.0
1.5
2.0
2.5
0.0
0.5
1.0
1.5
2.0
2.5
V
(V)
V
(V)
in
in
Voltage-transfer characteristics with hysteresis.
The effect of varying the ratio of the
PMOS device
M
. The width is
k
* 0.5 m.
m
4

---
CMOS Schmitt Trigger (2)
CMOS Schmitt Trigger (2)

---
Multivibrator Circuits
Multivibrator Circuits

---
Transition-Triggered Monostable
Transition-Triggered Monostable

---
Monostable Trigger (RC-based)
Monostable Trigger (RC-based)

---
Astable Multivibrators (Oscillators)
Astable Multivibrators (Oscillators)
0
1
2
N-1
Ring Oscillator
simulated response of 5-stage oscillator

---
Relaxation Oscillator
Relaxation Oscillator

---
Voltage Controller Oscillator (VCO)
Voltage Controller Oscillator (VCO)

---
Differential Delay Element and VCO
Differential Delay Element and VCO
two stage VCO
simulated waveforms of 2-stage VCO
in
2
v
1
v
2
v
3
v
4
V
ctrl
V
o
2
V
o
1
in
1
delay cell
0.5
0.0
0.5
1.0
1.5
2.0
2.5
3.0
2
0.5
1.5
V
1
V
2
V
3
V
4
time (ns)
2.5
3.5