Digital Integrated Circuits A Design Perspective
Digital Integrated Circuits
A Design Perspective
Jan M. Rabaey
Anantha Chandrakasan
Borivoje Nikolic
The Wire
July 30, 2002

---
The Wire
The Wire
schematics
physical

---
Interconnect Impact on Chip
Interconnect Impact on Chip

---
Wire Models
Wire Models
Capacitance-only
All-inclusive model

---
Impact of Interconnect Parasitics
Impact of Interconnect Parasitics
Interconnect parasitics
  - reduce reliability
  - affect performance and power consumption
Classes of parasitics
  - Capacitive
  - Resistive
  - Inductive

---
Nature of Interconnect
Nature of Interconnect
Global Interconnect
S
Local
= S
Technology
S
Global
= S
Die
Source: Intel

---
INTERCONNECT
INTERCONNECT
Capacitance

---
Capacitance of Wire Interconnect
Capacitance of Wire Interconnect

---
Capacitance: The Parallel Plate Model
Capacitance: The Parallel Plate Model
size 12{c rSub { size 8{ bold "int"} } = { {ε rSub { size 8{ ital "di"} } } over {t rSub { size 8{ ital "di"} } } } ital "WL"} {}
size 12{S rSub { size 8{ ital "Cwire"} } = { {S} over {S cdot S rSub { size 8{L} } } } = { {1} over {S rSub { size 8{L} } } } } {}

---
Permittivity
Permittivity

---
Fringing Capacitance
Fringing Capacitance

---
Fringing versus Parallel Plate
Fringing versus Parallel Plate

---
Interwire Capacitance
Interwire Capacitance

---
Impact of Interwire Capacitance
Impact of Interwire Capacitance

---
Wiring Capacitances (0.25 mm CMOS)
Wiring Capacitances (0.25 m CMOS)

---
INTERCONNECT
Resistance

---
Wire Resistance
Wire Resistance

---
Interconnect Resistance
Interconnect Resistance

---
Dealing with Resistance
Dealing with Resistance
- Selective Technology Scaling
- Use Better Interconnect Materials
  - reduce average wire-length
  - e.g. copper, silicides
More Interconnect Layers
  - reduce average wire-length

---
Polycide Gate MOSFET
Polycide Gate MOSFET
Silicide
PolySilicon
SiO
2
+
+
n
n
p
Silicides: WSi
2,
TiSi
2
, PtSi
2
and TaSi
Conductivity: 8-10 times better than Poly

---
Sheet Resistance
Sheet Resistance

---
Modern Interconnect
Modern Interconnect

---
Example: Intel 0.25 micron Process
Example: Intel 0.25 micron Process
5 metal layers
Ti/Al - Cu/Ti/TiN
Polysilicon dielectric

---
INTERCONNECT
Inductance

---
Interconnect
Modeling

---
The Lumped Model
The Lumped Model

---
The Lumped RC-Model The Elmore Delay
The Lumped RC-Model
The Elmore Delay

---
The Ellmore Delay RC Chain
The Ellmore Delay
RC Chain

---
Wire Model
Wire Model
Assume: Wire modeled by N equal-length segments
For large values of N:

---
The Distributed RC-line
The Distributed RC-line
The diffusion equation

---
Step-response of RC wire as a function of time and space
Step-response of RC wire as a function of time and space

---
RC-Models
RC-Models

---
Driving an RC-line
Driving an RC-line

---
Design Rules of Thumb
Design Rules of Thumb
rc delays should only be considered when tpRC >> tpgate of the driving gate
  Lcrit >>  tpgate/0.38rc
rc delays should only be considered when the rise (fall) time at the line input is smaller than RC, the rise (fall) time of the line
  trise < RC
  - when not met, the change in the signal is slower than the propagation delay of the wire
© MJIrwin, PSU, 2000