4. VAJA: SIMULACIJA KONTINUIRNEGA BIOPROCESA

Datum:	1.12.2006

- OSNOVE

Imamo bioreaktor, kjer je Fv=Fiz, zato je . Zaradi poenostavitve predpostavimo idealno pomešanje c(v reaktorju)=ciz.

( zaradi tega, ker je odvisno ali pišemo bilanco za S ali P)

Glede na to, da je v stacionarnem stanju  (dV=0, dc=0), velja

{Example BIOREACT}

{Fermentation in a bioreactor either batch, fedbatch or continuous.}

{The flow rates F0 and F1 need to be set correctly for each reactor type.}

{Flow rates are initially set to zero. They can be switched on by

changing their values.  A chemostat would have F0=F1, a batch reactor F0=F1=0 and a fedbatch F1=0}

{A steady state X-D curve for a chemostat can be made using the Parametric Run feature, but the statement F1=F0 needs to be activated in the program by removing the brackets.  Make sure the steady state is actually reached.}

{Biokinetic parameters}

UM=0.3	{Specific growth rate, 1/h}

KS=0.1	{Monod saturation constant, kg/m3}

K1=0.003	{Non-growth associated product constant, 1/h}

K2=0.008	{Growth associated product constant, kg product/kg biomass}

Y=0.8	{Yield constant,  kg biomass/kg substrate}

{Feed and flow conditions}

SF=10	{Substrate conc. in feed, kg/m3}

F0=0.1	{Feed flow rate, m3/h}

F1=0	{Outlet flow rate, m3/h}

METHOD Auto

STARTTIME=0

STOPTIME=50

- NALOGA

S pomočjo računalniške simulacija kontinuirnega procesa s spreminjanjem D poiskati vrednost, pri kateri izpiramo biomaso, določiti stacionarne vrednosti X in S, ter čas, potreben za vzpostavitev stacionarnega stanja.

- APARATURA

Računalnik in program Berkeley Madonna.

- MERITVE IN IZRAČUNI

F0=F1

spreminjali smo F0:

| krivulja | 1 | 2 | 3 | 4 | 5 |
| --- | --- | --- | --- | --- | --- |
| F0=F1= | 0,1 | 0,2 | 0,25 | 0,29 | 0,30 |

Ker je D=F/V, smo z večanjem F (pri konstantnem V) torej večali tudi D

Vidimo, da se z večanjem F0 začne izpiranje biomase (X), najhitreje je to pri F0=0.3.

Ko pride do izpiranja biomase, pride tudi do izpiranja substrata.