4. VAJA: SIMULACIJA KONTINUIRNEGA BIOPROCESA

Datum:	1.12.2006

OSNOVE

Imamo bioreaktor, kjer je Fv=Fiz, zato je size 12{ { { ital "dV"} over { ital "dt"} } =0} {} . Zaradi poenostavitve predpostavimo idealno pomešanje c(v reaktorju)=ciz.
size 12{ { {d \( ital "cV" \) } over { ital "dt"} } =F rSub { size 8{V} } c rSub { size 8{V} } - F rSub { size 8{ ital "iz"} } c rSub { size 8{ ital "iz"} } +- ital "rV"} {} ( size 12{ +- {}} {} zaradi tega, ker je odvisno ali pišemo bilanco za S ali P)
Glede na to, da je v stacionarnem stanju size 12{ { {d \( ital "cV" \) } over { ital "dt"} } =c { { ital "dV"} over { ital "dt"} } +V { { ital "dc"} over { ital "dt"} } =0} {} (dV=0, dc=0), velja size 12{F rSub { size 8{V} } c rSub { size 8{V} } =F rSub { size 8{ ital "iz"} } c rSub { size 8{ ital "iz"} } +- ital "rV"} {}

{Example BIOREACT}

{Fermentation in a bioreactor either batch, fedbatch or continuous.}
{The flow rates F0 and F1 need to be set correctly for each reactor type.}

{Flow rates are initially set to zero. They can be switched on by
changing their values. A chemostat would have F0=F1, a batch reactor F0=F1=0 and a fedbatch F1=0}

{A steady state X-D curve for a chemostat can be made using the Parametric Run feature, but the statement F1=F0 needs to be activated in the program by removing the brackets. Make sure the steady state is actually reached.}

{Biokinetic parameters}
UM=0.3	{Specific growth rate, 1/h}
KS=0.1	{Monod saturation constant, kg/m3}
K1=0.003	{Non-growth associated product constant, 1/h}
K2=0.008	{Growth associated product constant, kg product/kg biomass}
Y=0.8	{Yield constant, kg biomass/kg substrate}

{Feed and flow conditions}
SF=10	{Substrate conc. in feed, kg/m3}
F0=0.1	{Feed flow rate, m3/h}
F1=0	{Outlet flow rate, m3/h}

METHOD Auto
STARTTIME=0
STOPTIME=50

NALOGA

S pomočjo računalniške simulacija kontinuirnega procesa s spreminjanjem D poiskati vrednost, pri kateri izpiramo biomaso, določiti stacionarne vrednosti X in S, ter čas, potreben za vzpostavitev stacionarnega stanja.

APARATURA

Računalnik in program Berkeley Madonna.
MERITVE IN IZRAČUNI

F0=F1
spreminjali smo F0:
krivulja	1	2	3	4	5
F0=F1=	0,1	0,2	0,25	0,29	0,30

Ker je D=F/V, smo z večanjem F (pri konstantnem V) torej večali tudi D

Vidimo, da se z večanjem F0 začne izpiranje biomase (X), najhitreje je to pri F0=0.3. (natančno 0,29698599)
Ko pride do izpiranja biomase, pride tudi do izpiranja substrata.