Nivoji podrobnosti  Level of Detail (LOD)
Nivoji podrobnosti
Level of Detail (LOD)

---
Problem s podrobnostmi
Problem s podrobnostmi
Grafični sistemi so preplavljeni s podatki o modelih
  - Zelo podrobne podatkovne baze CAD
  - Zelo natančna skeniranja ploskev
Viri, ki so na voljo, so omejeni
  - CPE, prostor, hitrost grafike, Pasovna širina omrežja
Potrebujemo bolj ekonomične modele
  - Želimo najmanjši nivo podrobnosti (level of detail, LOD), ki še zadošča

---
LOD in interaktivnost
LOD in interaktivnost
Nivo podrobnosti (LOD) je pomembna tehnika za zagotavljanje interaktivnosti
  - Kompromis med vernostjo in učinkovitostjo
  - Ni edina tehnikal! Je komplement:
    - Vzporednem upodabljanju
    - Izločanju zakritih stvari
    - Upodabljanju na nivoju slike (image-based rendering)
    - itd...

---
Omejitve vida
Omejitve vida
Visual acuity
  - Retina can resolve detail of around 0.5 min of arc
  - 130 million photoreceptors / 1 million ganglion cells
Peripheral Vision
  - Highest sensitivity to spatial detail at fovea	(the central 4 to 5 degrees of vision)
  - 35-fold reduction from fovea  periphery
Motion Sensitivity
  - Eye less sensitive to detail moving across retina
  - Fast moving objects become “blurred”

---
Visual Perception Software
Visual Perception Software
Vermeer
“Officer and Laughing Girl”, 1658-60
120 x 135 degrees FOV
No eccentricity blurring
No velocity blurring

---
Visual Perception Software
Vermeer
“Officer and Laughing Girl”, 1658-60
120 x 135 degrees FOV
Eccentricity blurring
No velocity blurring

---
Visual Perception Software
Vermeer
“Officer and Laughing Girl”, 1658-60
120 x 135 degrees FOV
Eccentricity blurring
Velocity = 60 deg/s

---
Modeliranje omejitev vida
Modeliranje omejitev vida
- Results of Contrast Grating tests can be modeled with a Contrast Sensitivity Function
- CSF defines the bandwidth of vision

---
Faktorji CSF
Faktorji CSF
Background illumination
  - Contrast sensitivity degrades in dim conditions
Display Device Settings
  - Brightness, contrast, color, and gamma
Viewer’s level of light adaption
  - Photoreceptor range and pupil dilation controlled by a feedback loop
Viewer’s visual system efficiency
  - e.g., myopia causes light to converge in front of retina
Viewer’s age
  - Contrast sensitivity less developed in infants & declines with old age

---
Faktorji CSF (nadaljevanje)
Faktorji CSF (nadaljevanje)
Viewer’s emotional state
  - Affects dilation of pupils: smaller pupil = less light = drop in visual acuity
Auditory Stimuli?
  - Recent Nature paper shows visual perception affected by a adding an audible beep during task
Therefore, perceptual data are normally based upon a “Standard Observer”, assuming ideal environmental and viewer conditions.

---
LOD:  osnovna zamisel
LOD: osnovna zamisel
The problem:
  - Geometric datasets can be too complex to render at interactive rates
One solution:
  - Simplify the polygonal geometry of small or distant objects
  - Known as Level of Detail or LOD
    - polygonal simplification, geometric simplification, mesh reduction, decimation, multiresolution modeling, …

---
Tvorba LOD za predmete
Tvorba LOD za predmete
69,451 poligonov
2,502 poligonov
251 poligonov
76 poligonov

---
LOD: Vprašanja
LOD: Vprašanja
- How to represent and generate simpler versions of a complex model?
- How to evaluate the fidelity of the simplified models?
- When to use which LOD of an object?
69,451 poligonov
2,502 poligonov
251 poligonov
76 poligonov

---
Oddaljeni predmeti - bolj grob nivo podrobnosti
Oddaljeni predmeti - bolj grob nivo podrobnosti

---
LOD in oddaljenost
LOD in oddaljenost
d1
d2
Select resolution based upon the distance between an element and the viewpoint, i.e. coarser resolution for distant geometry.
  - Simple to calculate (3-D Euclidean distance)
  - Scale dependent
  - Resolution dependent
  - Field of View dependent

---
Velikost in LOD
Velikost in LOD
Select resolution based upon the projected screen size (or area) of an element. Objects appear smaller as they move further away.
  - Requires 3-D  2-D projection
  - Scale invariant
  - Resolution invariant
  - Field of View invariant
Bounding spheres or ellipsoids normally used instead of boxes as more efficient to calculate projected extent

---
Ekscentričnost in  LOD
Ekscentričnost in LOD
  - Resolution is selected based upon the degree to which an element exists in the visual periphery, i.e. display elements that the user is looking at in high resolution.
  - Humans can resolve less detail in their peripheral field due to:
    - more retinal photoreceptors (rods/cones) towards fovea
    - retinal and cortical cell receptive field sizes increases linearly with eccentricity
    - 80% of cortical cells devoted to central 10 degrees of vision
  - Use eye tracking system to track user’s gaze or assume user looking towards center of display


---
Hitrost in LOD
Hitrost in LOD
  - olution based upon the angular velocity of an element across the visual field, i.e. faster moving objects appear in lower resolution
  - Humans can resolve less spatial detail in objects moving across the retina, causing objects to blur as they move/ rotate, or the user’s gaze moves
  - It is believed visual information for small features are destroyed by the process of integrating stimulus energy over time
  - Without eye tracking technology, assume angular velocity across display device
1 deg/s
20 deg/s

---
Globina polja in LOD
Globina polja in LOD
Panum’s fusional area
  - Resolution of element dependent upon the depth of field focus of the user’s eyes, i.e. objects out with the fusional area appear in lower detail
  - Under binocular vision, both eyes converge on object at certain distance in order to focus retinal image
  - Objects in front or behind this fusional area are unfocused, suffering from double images
  - Must track both eyes accurately	to evaluate convergence distance

---
Povzetek
Povzetek
Primary LOD selection criteria
  - Distance or Size
  - Velocity
  - Eccentricity
  - Depth of Field
- Additional LOD constraints
  - Fixed-frame rate schedulers (reactive or predictive)
  - Hysteresis (switching lag)
  - Priority schemes
  - Alpha-blended transitions (fading regions)
  - Geomorph transitions (morph geometry)

---
Statična resolucija ne zadošča
Statična resolucija ne zadošča
Model used in variety of contexts
  - many machines; variable capacity
  - projected screen size will vary
Context dictates required detail
  - LOD should vary with context
  - context varies over time
  - with what level of coherence?
    - generally high coherence in view
    - possibly poor coherence in load

---
Potrebujemo večresolucijske modele(Multiresolution Models)
Potrebujemo večresolucijske modele(Multiresolution Models)
Encode wide range of levels of detail
  - extract appropriate approximations at run time
  - must have low overhead
    - space consumed by representation
    - cost of changing level of detail while rendering
  - can be generated via simplification process
Image pyramids (mip-maps) a good example
  - very successful technique for raster images

---
Zgradba LOD
Zgradba LOD
Discrete LOD
  - Generate a handful of LODs for each object
Continuous LOD (CLOD)
  - Generate data structure for each object from which a spectrum of detail can be extracted
View-dependent LOD
  - Generate data structure from which an LOD specialized to the current view parameters can be generated on the fly.
  - One object may span multiple levels of detail
Hierarchical LOD
  - Aggregate objects into assemblies with their own LODs

---
Discrete Multiresolution Models
Discrete Multiresolution Models
Given a model, build a set of approximations
  - can be produced by any simplification system
  - at run time, simply select which to render
Inter-frame switching causes “popping”
  - can smooth transition with image blending
  - or use geometry blending: geomorphing [Hoppe]
Supported by several software packages

---
Tradicionalni pristop: Diskretni nivo podrobnosti
Tradicionalni pristop: Diskretni nivo podrobnosti
Traditional LOD in a nutshell:
  - Create LODs for each object separately in a preprocess
  - At run-time, pick each object’s LOD according to the object’s distance (or
    similar criterion)
Since LODs are created offline at fixed resolutions, we call this discrete LOD

---
Diskretni LOD:Prednosti
Diskretni LOD:Prednosti
Simplest programming model; decouples simplification and rendering
  - LOD creation need not address real-time rendering constraints
  - Run-time rendering need only pick LODs
Fits modern graphics hardware well
  - Easy to compile each LOD into triangle strips, display lists, vertex arrays, …
  - These render much faster than unorganized triangles on today’s hardware (3-5 x)

---
Diskretni LOD:Slabosti
Diskretni LOD:Slabosti
So why use anything but discrete LOD?
Answer: sometimes discrete LOD not suited for drastic simplification
Some problem cases:
Terrain flyovers
Volumetric isosurfaces
Super-detailed range scans
Massive CAD models

---
Poenostavljanje: problem velikih objektov
Poenostavljanje: problem velikih objektov

---
Poenostavljanje: problem majhnih objektov
Poenostavljanje: problem majhnih objektov

---
Limits of Discrete Models
Limits of Discrete Models
We may need varying LOD over surface
  - large surface, oblique view (eg. on terrain)
    - need high detail near the viewer
    - need less detail far away
  - single LOD will be inappropriate
    - either excessively detailed in the distance (wasteful)
    - or insufficiently detailed near viewer (visual artifacts)
Doesn’t really exploit available coherence
  - small view change may cause large model change

---
Poenostavljanje
Poenostavljanje
For drastic simplification:
  - Large objects must be subdivided
  - Small objects must be combined
Difficult or impossible with discrete LOD

---
Choosing LODs:LOD Run-Time Management
Choosing LODs:LOD Run-Time Management
Fundamental LOD issue: where in the scene to allocate detail?
  - For discrete LOD this equates to choosing which LOD will represent each object
  - Run every frame on every object; keep it fast

---
Choosing LODs
Choosing LODs
Describe a simple method for the system to choose LODs
  - Assign each LOD a range of distances
  - Calculate distance from viewer to object
  - Use corresponding LOD
How might we implement this in a scene-graph based system?

---
Implementacija preklapljanja LOD
Implementacija preklapljanja LOD

---
Implementacija preklapljanja LOD

---
Implementacija mehkega prehoda LOD
Implementacija mehkega prehoda LOD

---
Primerjava preklapljanja in prehoda
Primerjava preklapljanja in prehoda

---
Mehki prehod
Mehki prehod

---
Choosing LODs
What’s wrong with this simple approach?
  - Visual “pop” when switching LODs can be disconcerting
  - Doesn’t maintain constant frame rate; lots of objects still means slow frame times
  - Requires someone to assign switching distances by hand
  - Correct switching distance may vary with field of view, resolution, etc.
What can we do about each of these?

---
Choosing LODs Maintaining constant frame rate
Choosing LODs Maintaining constant frame rate
One solution: scale LOD switching distances by a “bias”
  - Implement a feedback mechanism:
    - If last frame took too long, decrease bias
    - If last frame took too little time, increase bias
  - Dangers:
    - Oscillation caused by overly aggressive feedback
    - Sudden change in rendering load can still cause overly long frame times

---
Choosing LODs: Maintaining constant frame rate
Choosing LODs: Maintaining constant frame rate
- A better (but harder) solution: predictive LOD selection
- For each LOD estimate:
  - Cost (rendering time)
  - Benefit (importance to the image)

---
Choosing LODs: Maintaining constant frame rate
- A better (but harder) solution: predictive LOD selection
- For each LOD estimate:
  - Cost (rendering time)
    - # of polygons
    - How large on screen
    - Vertex processing load (e.g., lighting) OR
    - Fragment processing load (e.g., texturing)
  - Benefit (importance to the image)

---
Choosing LODs: Maintaining constant frame rate
- A better (but harder) solution: predictive LOD selection
- For each LOD estimate:
  - Cost (rendering time)
  - Benefit (importance to the image)
    - Size: larger objects contribute more to image
    - Accuracy: no of verts/polys, shading model, etc.
    - Priority: account for inherent importance
    - Eccentricity: peripheral objects harder to see
    - Velocity: fast-moving objects harder to see
    - Hysteresis: avoid flicker; use previous frame state

---
Zvezni nivo podrobnosti
Zvezni nivo podrobnosti
A departure from the traditional discrete approach:
  - Discrete LOD: create individual levels of detail in a preprocess
  - Continuous LOD: create data structure from which a desired level of detail can be extracted at run time.

---
Zvezni LOD:prednosti
Zvezni LOD:prednosti
Better granularity  better fidelity
  - LOD is specified exactly, not chosen from a few pre-created options
  - Thus objects use no more polygons than necessary, which frees up polygons for other objects
  - Net result: better resource utilization, leading to better overall fidelity/polygon
Better granularity  smoother transitions
  - Switching between traditional LODs can introduce visual “popping” effect
  - Continuous LOD can adjust detail gradually and incrementally, reducing visual pops
    - Can even geomorph the fine-grained simplification operations over several frames to eliminate pops

---
Zvezni LOD:prednosti
Supports progressive transmission
  - Progressive Meshes [Hoppe 97]
  - Progressive Forest Split Compression [Taubin 98]
Leads to view-dependent LOD
  - Use current view parameters to select best representation for the current view
  - Single objects may thus span several levels of detail

---
View-Dependent LOD: Primeri
View-Dependent LOD: Primeri
Show nearby portions of object at higher resolution than distant portions
View from eyepoint
Birds-eye view

---
View-Dependent LOD: Primeri
Show silhouette regions of object at higher resolution than interior regions

---
View-Dependent LOD:Primeri
View-Dependent LOD:Primeri
Show more detail where the user is looking than in their peripheral vision:
34,321 trikotnikov

---
View-Dependent LOD:primeri
View-Dependent LOD:primeri
Show more detail where the user is looking than in their peripheral vision:
11,726 trikotnikov

---
View-Dependent LOD:Prednosti
View-Dependent LOD:Prednosti
Even better granularity
  - Allocates polygons where they are most needed, within as well as among objects
  - Enables even better overall fidelity
Enables drastic simplification of very large objects
  - Example: stadium model
  - Example: terrain flyover

---
Streaming over the Web
Streaming over the Web
TerraVision (SRI)
Yosemite Park
San Francisco Bay

---
Hierarhični LOD
Hierarhični LOD
- View-dependent LOD solves the
  Problem With Large Objects
- Hierarchical LOD can solve the
  Problem With Small Objects
  - Merge objects into assemblies
  - At sufficient distances, simplify assemblies, not individual objects
  - How to represent this in a scene graph?

---
Hierarhični LOD
Hierarchical LOD dovetails nicely with view-dependent LOD
  - Treat the entire scene as a single object to be simplified in view-dependent fashion
Hierarchical LOD can also sit atop traditional discrete LOD schemes

---
Izbira LODs: Upravljanje LOD v realnem času
Izbira LODs: Upravljanje LOD v realnem času
Fundamental LOD issue: where in the scene to allocate detail?
  - For discrete LOD this equates to choosing which LOD will represent each object
  - Run every frame on every object; keep it fast

---
Izbira LOD
Izbira LOD
Describe a simple method for the system to choose LODs
  - Assign each LOD a range of distances
  - Calculate distance from viewer to object
  - Use corresponding LOD
How might we implement this in a scene-graph based system?

---
Izbira LOD
What’s wrong with this simple approach?
  - Visual “pop” when switching LODs can be disconcerting
  - Doesn’t maintain constant frame rate; lots of objects still means slow frame times
  - Requires someone to assign switching distances by hand
  - Correct switching distance may vary with field of view, resolution, etc.

---
Izbira LOD: vzdrževanje konstantnega števila slik (frame rate)
Izbira LOD: vzdrževanje konstantnega števila slik (frame rate)
One solution: scale LOD switching distances by a “bias”
  - Implement a feedback mechanism:
    - If last frame took too long, decrease bias
    - If last frame took too little time, increase bias
  - Dangers:
    - Oscillation caused by overly aggressive feedback
    - Sudden change in rendering load can still cause overly long frame times

---
Avtomatska poenostavitev ploskev
Avtomatska poenostavitev ploskev

---
Avtomatska poenostavitev ploskev
Produce approximations with fewer triangles
  - should be as similar as possible to original
  - want computationally efficient process
Need criteria for assessing model similarity
  - for display, visual similarity is the ultimate goal
  - similarity of shape is often used instead
    - generally easier to compute
    - lends itself more to applications other than display

---
Fokus na poligonskih modelih
Fokus na poligonskih modelih
Polygonal surfaces are ubiquitous
  - only primitive widely supported in hardware
  - near-universal support in software packages
  - output of most scanning systems
Switching representations is no solution
  - indeed, some suffer from the same problem
  - many applications want polygons
Will always assume models are triangulated

---
Druga področja
Druga področja
Geometry compression
  - simplification is a kind of lossy compression
Surface smoothing
  - reduces geometric complexity of shape
Mesh generation
  - finite element analysis (e.g., solving PDE’s)
  - need appropriate mesh for good solution
  - overly complex mesh makes solution slow

---
Pregled metod poenostavljanja
Pregled metod poenostavljanja
Manual preparation has been widely used
  - skilled humans produce excellent results
  - very labor intensive, and thus costly
Most common kinds of automatic methods
  - vertex clustering
  - vertex decimation
  - iterative contraction

---
Tvorba LOD
Tvorba LOD
Simplification operator:
  - Cell collapse
  - Vertex removal
  - Edge collapse
    - Full edge collapse
      - Better fidelity (show why)
    - Half edge collapse
      - Less memory
      - Sort vertices, tris into VAR array for fast rendering
    - Vertex-pair merge a.k.a. “virtual edge collapse”
      - Merge separate objects

---
Optimalni približki
Optimalni približki
Achieve given error with fewest triangles
  - no mesh with fewer triangles meets error limit
Computationally feasible for curves
  - O(n) for functions of one variable
  - but O(n2 log n) for plane curves
Intractable for surfaces
  - NP-hard to find optimal height field [Agarwal–Suri 94]
  - must also be the case for surfaces

---
Združevanje verteksov
Združevanje verteksov
Partition space into cells
  - grids [Rossignac-Borrel], spheres [Low-Tan], octrees, ...
Merge all vertices within the same cell
  - triangles with multiple corners in one cell will degenerate

---
Zmanjševanje števila verteksov
Zmanjševanje števila verteksov
Starting with original model, iteratively
  - rank vertices according to their importance
  - select unimportant vertex, remove it, retriangulate hole
A fairly common technique

---
Iterativno krčenje robov
Iterativno krčenje robov
Contraction can operate on any set of vertices
  - edges (or vertex pairs) are most common, faces also used
Starting with the original model, iteratively
  - rank all edges with some cost metric
  - contract minimum cost edge
  - update edge costs

---
Krčenje robov
Krčenje robov
Single edge contraction (v1,v2)  v’ is performed by
  - moving v1 and v2 to position v’
  - replacing all occurrences of v2 with v1
  - removing v2 and all degenerate triangles
v’
v2
v1

---
Algoritem rušenja robov
Algoritem rušenja robov
V2
V2
Collapse
V1

---
Algoritem rušenja robov
Sort all edges (by some metric)
repeat
  Collapse edge
  choose edge vertex (or compute optimal vertex)
  Fix-up topology
until (no edges left)

---
Iterativno krčenje robov
Currently the most popular technique
  - simpler operation than vertex removal
  - well-defined on any simplicial complex
Also induces hierarchy on the surface
  - a very important by-product
  - enables several multiresolution applications

---
Prednosti rušenja robov
Prednosti rušenja robov
- Edge collapse operation is simple
- Supports non-manifold topology:

---
Ohranjevanje mej
Ohranjevanje mej
- To preserve important boundaries, label edges as normal or discontinuity
- For each face with a discontinuity, a plane perpendicular intersecting the discontinuous edge is formed.
- These planes are then converted into quadrics, and can be weighted more heavily with respect to error value.

---
Preprečevanje inverzije mreže
Preprečevanje inverzije mreže
Preventing foldovers:
- Calculate the adjacent face normals, then test if they would flip after simplification
- If so, that simplification can be weighted heavier or disallowed.
7
8
2
10
A
6
9
merge
3
1
4
5
10
5
4
6
3
2
8
9
A

---
Krčenje parov verteksov
Krčenje parov verteksov
Can also easily contract any pair of vertices
  - fundamental operation is exactly the same
  - joins previously unconnected areas
  - can be used to achieve topological simplification

---
Rušenje robov : združevanje parov verteksov
Rušenje robov : združevanje parov verteksov
Even better: vertex-pair merging merges two vertices that:
  - Share an edge, or
  - Are within some threshold distance t

---
View-Dependent LOD: Algoritmi
View-Dependent LOD: Algoritmi
Many good published algorithms:
  - Progressive Meshes by Hoppe
    Merge Trees by Xia & Varshney [Visualization 96]
  - Hierarchical Dynamic Simplification by Luebke & Erikson Multitriangulation by DeFloriani et al
  - Others…

---
Pregled: Algoritem VDS
Pregled: Algoritem VDS
Overview of the VDS algorithm:
  - A preprocess builds the vertex hierarchy,
    a hierarchical clustering of vertices
  - At run time, clusters appear to grow and shrink as the viewpoint moves
  - Clusters that become too small are collapsed, filtering out some triangles

---
Vertex Hierarchies
Vertex Hierarchies
A cut through the tree
  - contract all below cut
  - leaves are “active”
  - determines partition
  - and an approximation
Encodes dependencies
  - PM’s assume total order
  - disjoint subtrees indep.
  - get novel approximations
  - but must avoid fold-over

---
Podatkovne strukture
Podatkovne strukture
The vertex hierarchy
  - Represents the entire model
  - Hierarchy of all vertices in model
  - Queried each frame for updated scene
The active triangle list
  - Represents the current simplification
  - List of triangles to be displayed
  - Triangles added and deleted by operations on vertex tree

---
Vertex Hierarchies for View-Dependent Refinement
Vertex Hierarchies for View-Dependent Refinement
Multiresolution representation for display
  - incrementally move cut between frames
    [Xia-Varshney, Hoppe, Luebke-Erickson]
  - move up/down where less/more detail needed
  - relies on frame-to-frame coherence
  - can accommodate geomorphing
Common application of vertex hierarchy
  - hierarchy only guides active front evolution
  - more flexibility & overhead vs. discrete multires

---
Hierarhija verteksov
Hierarhija verteksov
Each node in vertex hierarchy supports a subset of the model vertices
  - Leaf nodes support a single vertex from the original full-resolution model
  - The root node supports all vertices
For each node we also assign a representative vertex or proxy

---
Drevo verteksov: Zapiranje in odpiranje
Drevo verteksov: Zapiranje in odpiranje
- Folding a node collapses its vertices to the proxy
- Unfolding the node splits the proxy back into vertices
Fold Node A
Unfold Node A
3
1
2
9
8
7
10
5
4
6
A
9
8
10
5
4
6
A
3

---
Primer drevesa verteksov
Primer drevesa verteksov
8
7
R
A
2
D
E
10
6
9
3
10
A
B
C
3
1
1
2
7
4
5
6
8
9
4
5
Vertex hierarchy
Triangles in active list

---
Primer drevesa verteksov
8
R
A
D
E
10
6
9
3
10
A
B
C
3
1
2
7
4
5
6
8
9
4
5
Vertex hierarchy
Triangles in active list

---
Primer drevesa verteksov
8
R
A
D
E
10
6
9
3
10
A
B
C
3
B
1
2
7
4
5
6
8
9
4
5
Vertex hierarchy
Triangles in active list

---
Primer drevesa verteksov
8
R
A
D
E
10
9
3
10
A
B
C
3
B
1
2
7
4
5
6
8
9
Vertex hierarchy
Triangles in active list

---
Primer drevesa verteksov
8
R
A
C
D
E
10
9
3
10
A
B
C
3
B
1
2
7
4
5
6
8
9
Vertex hierarchy
Triangles in active list

---
Primer drevesa verteksov
R
A
C
D
E
10
3
10
A
B
C
3
B
1
2
7
4
5
6
8
9
Vertex hierarchy
Triangles in active list

---
Primer drevesa verteksov
R
A
C
E
D
E
10
3
10
A
B
C
3
B
1
2
7
4
5
6
8
9
Vertex hierarchy
Triangles in active list

---
Primer drevesa verteksov
R
A
E
D
E
10
10
A
B
C
3
B
1
2
7
4
5
6
8
9
Vertex hierarchy
Triangles in active list

---
Primer drevesa verteksov
R
A
D
E
D
E
10
10
A
B
C
3
B
1
2
7
4
5
6
8
9
Vertex hierarchy
Triangles in active list

---
Primer drevesa verteksov
R
D
E
D
E
10
A
B
C
3
B
1
2
7
4
5
6
8
9
Vertex hierarchy
Triangles in active list

---
Primer drevesa verteksov
R
D
E
D
E
R
10
A
B
C
3
B
1
2
7
4
5
6
8
9
Vertex hierarchy
Triangles in active list

---
Primer drevesa verteksov
R
D
E
R
10
A
B
C
3
1
2
7
4
5
6
8
9
Vertex hierarchy
Triangles in active list

---
Drevo verteksov
Drevo verteksov
At runtime, folds and unfolds create a cut or boundary across the vertex tree:
This part of the model
is represented at high detail
This part in low detail

---
Drevo verteksov:Livetris and Subtris
Drevo verteksov:Livetris and Subtris
Two categories of triangles affected:
8
7
Fold Node A
2
10
6
9
3
Unfold Node A
1
4
5
Node->Subtris: triangles that disappear upon folding
Node->Livetris: triangles that just change shape
9
8
10
5
4
6
A
3

---
Drevo verteksov:Livetris and Subtris
The key observation:
  - Each node’s subtris can be computed offline to be accessed quickly at run time
  - Each node’s livetris can be maintained at run time, or lazily evaluated upon rendering

---
View-Dependent Simplification
View-Dependent Simplification
- Any run-time criterion for folding and unfolding nodes may be used
- Examples of view-dependent simplification criteria:
  - Screenspace error threshold
  - Silhouette preservation
  - Triangle budget simplification
  - Gaze-directed perceptual simplification

---
Screenspace Error Threshold
Screenspace Error Threshold
Nodes chosen by projected area
  - User sets screenspace size threshold
  - Nodes which grow larger than threshold are unfolded

---
Ohranjevanje silhuet
Ohranjevanje silhuet
Retain more detail near silhouettes
  - A silhouette node supports triangles on the visual contour
  - Use tighter screenspace thresholds when examining silhouette nodes

---
Progressive Meshes
Progressive Meshes
We get more than just final approximation
  - sequence of contractions
  - corresponding intermediate approximations
Re-encode as progressive mesh (PM)
  - take final approximation to be base mesh
  - reverse of contraction sequence is split sequence
  - can reconstruct any intermediate model
  - allow for progressive transmission & compression

---
PM’s a Limited Multiresolution
PM’s a Limited Multiresolution
More flexibility is required
  - local addition/subtraction of triangles
    - as conditions change, make small updates in LOD
    - this is the multi-triangulation framework
    - may require novel approximations
Must encode dependency of contractions
  - PM’s imply dependency on earlier contractions
  - but we can reorder non-overlapping contractions

---
Triangle Budget Simplification
Triangle Budget Simplification
Minimize error within specified number of triangles
  - Sort nodes by screenspace error
  - Unfold node with greatest error, putting children into sorted list
  Repeat until budget is reached

---
Implementacija VDS: Optimizacije
Implementacija VDS: Optimizacije
Asynchronous simplification
  - Parallelize the algorithm
Exploiting temporal coherence
  - Scene changes slowly over time
Maintain memory coherent geometry
  - Optimize for rendering
  - Support for out-of-core rendering

---
Asinhrona poenostavitev
Asinhrona poenostavitev
- Algorithm partitions into two tasks:
- Run them in parallel
Render
Task
Simplify
Task
Vertex Tree
Active Triangle List
…

---
Asinhrona poenostavitev
If S = time to simplify, R = time to render:
  - Single process	= (S + R)
  - Pipelined	= max(S, R)
  - Asynchronous	= R
The goal: efficient utilization of GPU/CPU
  - e.g., NV_FENCE extension for asynchronous rendering

---
Časovna koherenca
Časovna koherenca
- Exploit the fact that frame-to-frame changes are small
- Three examples:
  - Active triangle list
  - Vertex tree
  - Budget-based simplification

---
Izkoriščanje časovne koherence
Izkoriščanje časovne koherence
Active triangle list
  - Could calculate active triangles every frame
  - But…few triangles are added or deleted
    each frame
  - Idea: make only incremental changes to an active triangle list
    - Simple approach: doubly-linked list of triangles
    - Better: maintain coherent arrays with swapping

---
Izkoriščanje časovne koherence
Vertex Tree
  - Few nodes change per frame
  - Don’t traverse whole tree
  - Do local updates only
    at boundary nodes
Unfolded
Nodes
Boundary Nodes

---
Časovna koherenca: Triangle Budget Simplification
Časovna koherenca: Triangle Budget Simplification
Exploiting temporal coherence in budget-based simplification
  - Start with tree from last frame, recalculate error for relevant nodes
  - Sort into two priority queues
    - One for potential unfolds, sorted on max error
    - One for potential folds, sorted on min error

---
Časovna koherenca: Triangle Budget Simplification
Then simplify:
  - While budget is met, unfold max node
    - This is the node whose folding has created the most error in the model
  - While budget is exceeded, fold min node
    - This is the node that introduces the least error when folded
  - Insert parents and children into queues
  Repeat until errormax < errormin

---
Optimizacija za upodabljanje
Optimizacija za upodabljanje
Idea: maintain geometry in coherent arrays
Active triangles
Inactive triangles
Unfolded nodes
Inactive nodes
Boundary nodes

---
Optimizacija za upodabljanje
Idea: use swaps to maintain coherence
Unfolded nodes
Boundary nodes
Inactive nodes
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
Fold node D:

---
Optimizacija za upodabljanje
Idea: use swaps to maintain coherence
Unfolded nodes
Boundary nodes
Inactive nodes
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
Fold node D:
Swap D with F

---
Optimizacija za upodabljanje
Idea: use swaps to maintain coherence
Unfolded nodes
Boundary nodes
Inactive nodes
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
Fold node D:
Swap D with F

---
Optimizacija za upodabljanje
Idea: use swaps to maintain coherence
Unfolded nodes
Boundary nodes
Inactive nodes
A
B
C
F
E
D
G
H
I
J
K
L
M
N
O
P
Q
Fold node D:
Swap D with F

---
Optimizacija za upodabljanje
Idea: use swaps to maintain coherence
Unfolded nodes
Boundary nodes
Inactive nodes
A
B
C
F
E
D
G
H
I
J
K
L
M
N
O
P
Q
Fold node D:
Move Unfolded/Boundary Marker

---
Optimizacija za upodabljanje
Idea: use swaps to maintain coherence
Unfolded nodes
Boundary nodes
Inactive nodes
A
B
C
F
E
D
G
H
I
J
K
L
M
N
O
P
Q
Fold node D:
Deactivate D’s children (swap w/ last boundary node)

---
Optimizacija za upodabljanje
Idea: use swaps to maintain coherence
Unfolded nodes
Boundary nodes
Inactive nodes
A
B
C
F
E
D
G
H
L
J
K
I
M
N
O
P
Q
Fold node D:
Deactivate D’s children (swap w/ last boundary node)

---
Optimizacija za upodabljanje
Idea: use swaps to maintain coherence
Unfolded nodes
Boundary nodes
Inactive nodes
A
B
C
F
E
D
G
H
L
J
K
I
M
N
O
P
Q
Fold node D:
Deactivate D’s children (swap w/ last boundary node)

---
Optimizacija za upodabljanje
Idea: use swaps to maintain coherence
Unfolded nodes
Boundary nodes
Inactive nodes
A
B
C
F
E
D
G
H
L
J
K
I
M
N
O
P
Q
Fold node D:
Deactivate D’s children (swap w/ last boundary node)

---
Optimizacija za upodabljanje
Idea: use swaps to maintain coherence
Unfolded nodes
Boundary nodes
Inactive nodes
A
B
C
F
E
D
G
K
L
J
H
I
M
N
O
P
Q
Fold node D:
Deactivate D’s children (swap w/ last boundary node)

---
Optimizacija za upodabljanje
Idea: use swaps to maintain coherence
Unfolded nodes
Boundary nodes
Inactive nodes
A
B
C
F
E
D
G
K
L
J
H
I
M
N
O
P
Q
Fold node D:
Deactivate D’s children (swap w/ last boundary node)

---
Optimizacija za upodabljanje : polja verteksov
Optimizacija za upodabljanje : polja verteksov
Biggest win: vertex arrays
  - Actually, keep separate parallel arrays for rendering data (coords, colors, etc)
Unfolded nodes
Boundary nodes
Inactive nodes
Vertex array!

---
Out-of-core Rendering
Out-of-core Rendering
Coherent arrays lend themselves to out-of-core simplification and rendering:
…
These need to be in memory…
These do not

---
Out-of-core Rendering
Coherent arrays lend themselves to out-of-core simplification and rendering:
  - Only need active portions of triangle and node arrays
  - Implement arrays as memory-mapped files
    - Let virtual memory system manage paging
    - A prefetch thread walks boundary nodes, bringing their children into memory to avoid glitches

---
Povzetek:  VDS Pros
Povzetek: VDS Pros
Supports drastic simplification!
  - View-dependent; handles the
    Problem With Large Objects
  - Hierarchical; handles the
    Problem With Small Objects
  - Robust; does not require (or preserve)
    mesh topology
- Rendering can be implemented efficiently using vertex arrays
- Supports rendering of models much larger than main memory

---
Povzetek:  VDS Cons
Povzetek: VDS Cons
- Increases CPU, memory overhead
- Hard to map efficiently onto GPU for efficient utilization
- Be aware of mesh foldovers
7
8
2
10
6
9
3
1
4
5

---
Povzetek: VDS Cons
Be aware of mesh foldovers:
7
8
2
10
A
6
9
3
1
4
5

---
Povzetek: VDS Cons
Be aware of mesh foldovers:
8
2
10
A
6
9
3
4
5

---
Povzetek: VDS Cons
Be aware of mesh foldovers:
  - These can be very distracting artifacts
  - Can prevent them at run-time
    - Add a normal-flipping test to fold criterion
    - Use a clever numbering scheme proposed by El-Sana and Varshney

---
View-Dependent Versus Discrete LOD
View-Dependent Versus Discrete LOD
View-dependent LOD is superior to traditional discrete LOD when:
  - Models contain very large individual objects (e.g., terrains)
  - Simplification must be completely automatic (e.g., complex CAD models)
  - Experimenting with view-dependent simplification criteria

---
View-Dependent Versus Discrete LOD
Discrete LOD is often the better choice:
  - Simplest programming model
  - Reduced run-time CPU load
  - Easier to leverage hardware:
    - Compile LODs into vertex arrays/display lists
    - Stripe LODs into triangle strips
    - Optimize vertex cache utilization and such

---
View-Dependent Versus Discrete LOD
Applications that may want to use:
  - Discrete LOD
    - Video games (but much more on this later…)
    - Simulators
    - Many walkthrough-style demos
  - Dynamic and view-dependent LOD
    - CAD design review tools
    - Medical & scientific visualization toolkits
    - Terrain flyovers (much more later…)

---
Continuous LOD:  The Sweet Spot?
Continuous LOD: The Sweet Spot?
Continuous LOD may be the right compromise on modern PC hardware
  - Benefits of fine granularity without the cost of view-dependent evaluation
  - Can be implemented efficiently with regard to
    - Memory
    - CPU
    - GPU

---
Merjenje napake
Merjenje napake
Most LOD algorithms measure error geometrically
  - What is the distance between the original and simplified surface?
  - What is the volume between the surfaces?
  - Etc
Really this is just an approximation to the actual visual error, which includes:
  - Color, normal, & texture distortion
  - Importance of silhouettes, background illumination, semantic importance, etc etc etc

---
Merjenje geometrične napake
Merjenje geometrične napake
- Hausdorff distance
- Average distance
- Surface-surface vs
  vertex-surface vs
  vertex-plane vs
  vertex-vertex
- Quadric error metrics: vertex-plane measure that works well in practice

---
Cena krčenja
Cena krčenja
Used to rank edges during simplification
  - reflects amount of geometric error introduced
  - main differentiating feature among algorithms
Must address two interrelated problems
  - what is the best contraction to perform?
  - what is the best position v’ for remaining vertex?
    - can just choose one of the endpoints
    - but can often do better by optimizing position of v’

---
Cena krčenja
Simple heuristics
  - edge length, dihedral angle, surrounding area, …
Sample distances to original surface
  - projection to closest point [Hoppe]
  - restricted projection [Soucy–Laurendeau, Klein et al, Ciampalini et al]
Alternative characterization of error
  - quadric error metrics [Garland–Heckbert]
  - local volume preservation [Lindstrom–Turk]

---
Measuring Error with Planes
Measuring Error with Planes
Each vertex has a (conceptual) set of planes
  - Error  sum of squared distances to planes in set
Initialize with planes of incident faces
  - Consequently, all initial errors are 0
When contracting pair, use plane set union
  - planes(v’) = planes(v1)  planes(v2)

---
A Simple Example: Contraction & “Planes” in 2D
A Simple Example: Contraction & “Planes” in 2D
Lines defined by neighboring segments
  - Determine position of new vertex
  - Accumulate lines for ever larger areas
v2
v1
v’
Original
After 1 Step

---
Measuring Error with Planes
Why base error on planes?
  - Faster, but less accurate, than distance-to-face
  - Simple linear system for minimum-error position
  - Efficient implicit form; no sets required
  - Drawback: unlike surface, planes are infinite
Related error metrics
  - Ronfard & Rossignac — max vs. sum
  - Lindstrom & Turk — similar form; volume-based

---
The Quadric Error Metric
The Quadric Error Metric
Given a plane, we can define a quadric Q
measuring squared distance to the plane as

---
The Quadric Error Metric
The Quadric Error Metric
Sum of quadrics represents set of planes
- Each vertex has an associated quadric
  - Error(vi) = Qi (vi)
  - Sum quadrics when contracting (vi, vj)  v’
  - Cost of contraction is Q(v’)

---
The Quadric Error Metric
Sum of endpoint quadrics determines v’
  - Fixed placement: select v1 or v2
  - Optimal placement: choose v’ minimizing Q(v’)
  - Fixed placement is faster but lower quality
  - But it also gives smaller progressive meshes
  - Fallback to fixed placement if A is non-invertible

---
Visualizing Quadrics in 3-D
Visualizing Quadrics in 3-D
Quadric isosurfaces
  - Are ellipsoids
    (maybe degenerate)
  - Centered around vertices
  - Characterize shape
  - Stretch in least-curved directions

---
Sample Model: Dental Mold
Sample Model: Dental Mold
50 sec
424,376 faces
60,000 faces

---
Sample Model: Dental Mold
55 sec
424,376 faces
8000 faces

---
Sample Model: Dental Mold
56 sec
424,376 faces
1000 faces

---
Must Also Consider Attributes
Must Also Consider Attributes
Mesh for solution
Radiosity solution

---
Must Also Consider Attributes
50,761 faces
10,000 faces

---
Simplification Summary
Simplification Summary
Spectrum of effective methods developed
  - high quality; very slow [Hoppe et al, Hoppe]
  - good quality; varying speed
    [Schroeder et al; Klein et al; Ciampalini et al; Guéziec
    Garland-Heckbert; Ronfard-Rossignac; Lindstrom-Turk]
  - lower quality; very fast [Rossignac–Borrel; Low–Tan]
  - result usually produced by transforming original
Various other differentiating factors
  - is topology simplified? restricted to manifolds?
  - attributes simplified or re-sampled into maps?

---
Applications Beyond Display
Applications Beyond Display
Other important applications are appearing
  - surface editing
  - surface morphing
  - multiresolution radiosity
Still others seem promising
  - hierarchical bounding volumes
  - object matching
  - shape analysis / feature extraction

---
Multiresolution Model Summary
Multiresolution Model Summary
Representations are available to support
  - progressive transmission
  - view-dependent refinement
  - hierarchical computation (e.g., radiosity)
But limitations remain
  - vertex hierarchies may over-constrain adaptation
  - adaptation overhead not suitable for all cases
  - interacting multiresolution objects ignored