PowerPoint Presentation
Družina Simatic

---
Programska oprema krmilnikov družine Simatic
LOGO! Soft Comfort za krmilnike LOGO!
STEP 7-Micro/WIN za krmilnike S7-200
STEP 7 za krmilnike S7-300 in S7-400

---
S7-200 Osnovni moduli
The S7-200 family comprises five different CPU types. The versions differ from one another primarily in terms of:
the number of integrated inputs and outputs
the size of the program and data storage and
upgradability

---
S7-200 Osnovni moduli
CPU 221
6 digitalnih vhodov
4 digitalni izhodi
ni razširljiv
the program storage capacity is 4 KB, data storage is 2 KB

---
S7-200 Osnovni moduli
CPU 222
8 digitalnih vhodov
6 digitalni izhodi
razširljiv do maksimalno digitalnih 78 I/O
two analog expansion modules enable the connection of 8 analog inputs and 4 analog outputs. The maximum number of analog values is 10
program storage has a capacity of 4 KB, the data storage, 2 KB.

---
S7-200 Osnovni moduli
CPU 224
14 digitalnih vhodov
10 digitalni izhodi
razširljiv do maksimalno digitalnih 168 I/O
28 analog  inputs and 14 analog outputs can be connected by means of seven analog expansion modules. The maximum number of analog values is 35
The data storage and program storage each have a capacity of  8 KB

---
S7-200 Osnovni moduli
CPU 224 XP
14 digitalnih vhodov
10 digitalni izhodi
razširljiv do maksimalno digitalnih 168 I/O
drugi komunikacijski interface (razlika napram CPU 224)
Two analog inputs and one analog output are already integrated
By means of seven analog  expansion modules, it is thus possible to implement 30 analog inputs and 15 analog outputs. The maximum number of analog connections is 38
The data storage amounts to 10 KB, the program storage, 12 KB.

---
S7-200 Osnovni moduli
CPU 226
24 digitalnih vhodov
16 digitalni izhodi
razširljiv do maksimalno digitalnih 248 I/O
drugi komunikacijski interface
28 analog  inputs and 14 analog outputs can be connected by means of seven analog expansion modules. The maximum number of analog ports is 35
The data storage has a capacity of 10 KB, the program storage 16 KB

---
S7-200 Osnovni moduli
Pregled vseh vrst CPU

---
S7-200 Osnovni moduli
Vrste CPU glede na napajanje
DC/DC/DC 24V
The CPU itself and the digital inputs are supplied with 24V DC. The transistor outputs are also switched electronically with 24V DC.
AC/DC/Relay
The CPU is supplied with 110/230V AC and the digital inputs with 24V DC. Relay outputs with a switching power of 2A.

---
S7-200 Osnovni moduli
Fizični izgled
razširitveno mesto (razen pri 221)

---
S7-200 Osnovni moduli
Fizični izgled
The CPU status LEDs show the CPU's current operating status at a glance
System error, or Diagnostics
RUN,
STOP

---
S7-200 Osnovni moduli
Fizični izgled
Vhodi in izhodi
An automation system is connected with the machine via the digital inputs and outputs. Signals from the field devices such as sensors and switches are monitored via the inputs; the outputs control pumps, motors or other devices.

---
S7-200 Osnovni moduli
Fizični izgled
Statusni indikatorji
The input and output status LEDs provide you with a visual indication of the current status of the integrated inputs an outputs.

---
S7-200 Osnovni moduli
Fizični izgled
Komunikacija
A maximum of 126 subscribers or nodes such as HMI systems, other CPUs or programming devices can be connected via the integrated RS-485 communication interface. The PPI protocol is used in homogenous S7-200 networks. In a network with TIA components such as S7-300 or S7-400, the S7-200 CPUs are integrated as MPI slaves.

---
S7-200 Osnovni moduli
Fizični izgled
Komunikacija
If the integrated interface is used with user specific protocols (free ASCII protocol) in FREEPORT mode, the CPU can accept any peripheral such as
printers
PC
Barcode readers

---
S7-200 Osnovni moduli
Fizični izgled
EPROM
An optional plug-in EEPROM memory module allows you to store CPU programs or to transfer programs from one CPU to another.

---
S7-200 Osnovni moduli
Fizični izgled
Dodatno baterijsko napajanje
An optional plug-in battery module allows you to back up internal data.

---
S7-200 Osnovni moduli
Fizični izgled
Urni modul
With the CPU 221 and CPU 222, there is an optional real-time clock module. This allows processing with time stamps on even the smallest members of the S7-200 family. Starting with the CPU 224, the system already possesses an integrated real-time clock.

---
S7-200 Osnovni moduli
Fizični izgled
Posebnosti CPU 224 XP
The CPU 224XP also has integrated analog I/Os.
Removal terminal strips for independent wiring are to be found with the 224, 224XP und 226 CPUs.
In addition, the CPU 224XP and CPU 226 come with a second communication interface.

---
S7-200 Razširitveni moduli
Način povezave
The expansion modules can give the S7-200:
additional functionality
increase the number of inputs and outputs.

---
S7-200 Razširitveni moduli
Način povezave
Up to two modules can be connected to the CPU 222 and up to seven modules to the CPU 224, 224XP and 226.
The CPU 221 is not expandable.
To accommodate space requirements, the S7-200 can also be layed out in two tiers.

---
S7-200 Razširitveni moduli
Moduli skupine EM 221 (digitalni-vhodi)
The EM 221 series expansion modules are equipped with digital inputs.
These exist in three versions:
8 digital inputs 24V DC
16 digital inputs 24V DC
8 digital inputs 120V/230V AC.

---
S7-200 Razširitveni moduli
Moduli skupine EM 222 (digitalni-izhodi)
The EM 222 expansion modules only come with digital outlets.
The EM 222 is available in four models:
4 transistor outputs 24V DC
8 transistor outputs 24V DC
4 x relays
8 x relays.

---
S7-200 Razširitveni moduli
Moduli skupine EM 223 (digitalni - vhodi in izhodi)
The EM 223 expansion modules come both with digital inputs and outputs.

---
S7-200 Razširitveni moduli
Moduli skupine EM 231 (analogni)
The EM 231 is equipped with four analog inputs.
The EM 232 with two analog outputs.
The EM 235 is equipped with four analog inputs and an analog output.

---
S7-200 Razširitveni moduli
Komunikacijski moduli

---
S7-200 Razširitveni moduli
Komunikacijski moduli
The EM 241 modem module connects the S7-200 with the telephone network. The S7-200 can thus be reached anywhere in the world or can actively send data and information of its own accord.
This enables you to carry out remote service. Remote inquiry and data transmission is of course also possible. The data transmission protocols are freely selectable e.g. SMS, Fax or Modbus RTU.

---
S7-200 Razširitveni moduli
Komunikacijski moduli
The PROFIBUS DP-Slave module EM 277 connects the S7-200 as a slave with a DP network. The transmission rate is up to 12 Mbit/s. The bus can support up to 99 devices whose station addresses are freely selectable via a rotary switch.

---
S7-200 Razširitveni moduli
Komunikacijski moduli
The CP 243-2 AS interface module converts the S7-200 into a powerful master on the AS-Interface. Up to 62 AS interface slaves can be connected to it.

---
S7-200 Razširitveni moduli
Komunikacijski moduli
The CP 243-1 Ethernet module makes it easy to attach an S7-200 to an industrial Ethernet. The Ethernet access is via the RJ45-connector. It supports remote programming, configuration and diagnosis as well as data transmission.
Simultaneous communication with up to 8 S7 PLCs, but also with an OPCserver for PC access, is possible.

---
S7-200 Razširitveni moduli
Komunikacijski moduli
The IT-Module CP 243-1 IT offers the same network functionality as the Ethernet module. Additionally, it is also enhanced with the Internet's functionality.
The module's IT functions allow you to implement your own homepage on the PLC or else use IT services such as E-Mail, File Transfer Protocol, etc.

---
S7-200 Razširitveni moduli
Specialni moduli
The EM 253 positioning model is used to control stepper motors. It issues its instructions to a power system which then executes the movement via a stepper motor.

---
S7-200 Razširitveni moduli
Specialni moduli
The EM 253 positioning model is used to control stepper motors. It issues its instructions to a power system which then executes the movement via a stepper motor.
The EM 253 can emit 12 to 200,000 impulses per second. It supports both jerk-free as well as linear accelerations and delays. The module supports other helpful and necessary additional functions such as for example various options for the reference point movement.

---
S7-200 Razširitveni moduli
Specialni moduli
The positioning wizard supports you in parameterizing and commissioning positioning tasks. This allows even complex procedural profiles to be implemented very easily.

---
S7-200 HMI moduli
Text Displays
Touch Panels
Operator Panels

---
S7-200 HMI moduli
Text display TD 200
The TD 200 features a two line, backlit text display for displaying message menus, text messages and other application data. 20 characters per line can be displayed.
The S7-200 can be networked easily with the TD 200 via PPI; the power supply is via the CPU. Alternatively, the device can be supplied from an external power source.

---
S7-200 HMI moduli
Touch panel TP 177micro

---
S7-200 HMI moduli
Panel OP 73 micro